## Slide 1: PID Controllers
Make Your Robots Move Smoothly and Accurately

## Slide 2: Why Control Systems Matter
Rovers veer off track or overshoot
Control systems maintain desired behavior (speed, position, heading)
Like Adaptive Cruise Control in cars
PID lets the robot self-correct using sensor feedback.

## Slide 3: Errors in a System
Examples:
  Target heading = 90°, robot is 70° → error = 20°
  Target arm angle = 500 ticks, current = 450 → error = 50
PID is a smart way to respond to errors

## Slide 4: PID
It’s a feedback control loop used to minimize error
Proportional (P): Responds to current error
Integral (I): Fixes accumulated past error
Derivative (D): Predicts future error
Analogy – maintain blue car at a set distance from the red car in cruise control

## Slide 5: Proportional (P) – Push harder when you are far
Big error → big correction
Small error → small correction
If your robot is way off the line, P makes it turn sharply back.
Problem: P alone causes overshoot & oscillation

## Slide 6: Integral (I) – Fix Long-term Biases
Adds up past error
Helps when robot almost reaches target but never quite does
Arm stops slightly below target every time. I slowly increases power to eliminate that gap
Problem: Too much I = robot goes crazy after delay.

## Slide 7: Derivative (D) – The Brake Pedal
Looks at how fast error is changing
Slows the robot as it approaches target
Without D: robot slams past target. With D: robot slows before reaching

## Slide 8: PID Equation
e(t) = error & Kp, Ki, Kd = tuning constants

## Slide 9: PID Equation

## Slide 10: PID in FTCLib

## Slide 11: Where to use PID
Arm position
Slides
Heading hold (gyro)
Driving straight
April Tag alignment

## Slide 12: PID Tuning - Steps
Start with P only
Increase P until oscillation
Add D to reduce oscillation
Add small I only if needed