## Slide 1: Rover Software
Mission to Mars

## Slide 2: What is FTC SDK?
Official programming framework for FIRST Tech Challenge
Written in Java and runs on Android phones
Provides:
  OpModes for control
  Access to hardware
  Telemetry for debug output
Think of it as the “default engine” to run your robot.

## Slide 3: What is FTCLib?
An open-source library built on top of the FTC SDK
Inspired by WPILib (used in FRC)
Encourages modular, reusable robot code
Provides:
  Subsystems
  Commands
  Controllers (PID, Feedforward, etc.)
Why use FTCLib? Cleaner code, better structure, easier debugging.

## Slide 4: OpModes – The Starting Point
An OpMode is the main entry point for running your robot
Two types:
  TeleOp (manual control)
  Autonomous (pre-programmed actions)

## Slide 5: Subsystems – Organize Your Robot
A Subsystem represents a part of your robot (e.g. drivetrain, arm, intake)
It holds hardware references and low-level methods

## Slide 6: Commands – Tell the Robot What to Do
A Command uses a Subsystem to perform an action
Can be:
  Run continuously (e.g., drive while joystick held)
  Run once (e.g., lift arm)

## Slide 7: Putting It All Together

## Slide 8: Benefits of Using FTCLib
Clean separation of logic
Easy to test and modify subsystems independently
Encourages good software engineering practices
Scales well as your robot gets more complex

## Slide 9: Resources and Next Steps
FTCLib GitHub: https://github.com/FTCLib/FTCLib
FTC SDK Docs: https://ftctechnh.github.io/ftc_app/doc/
M2M Source: https://github.com/acearun/MissionToMars
Practice:
  Turn your drivetrain into a subsystem
  Write a command for joystick control
  Try using CommandScheduler

## Slide 10: Controller Layout

## Slide 11: Exercise
Add a second motor and have its motion be controlled by the Left Joystick

## Slide 12: Exercise
Complete drivetrain build
Try Differential Tank & Arcade drives
Practice for runs