## Slide 1: Robotics Drive Trains & Motors
Day 2 – Mission to Mars

## Slide 2: What is a drive train?
It is the mechanical system that allows a robot to move by transmitting power from the motors to the wheels.
It controls the robot’s motion — including speed, direction, and maneuverability.
Main Components:
  Motors
  Wheels
  Gears / Gearboxes
  Chassis / Frame
Notes: Q: Why does the choice of drive train matter? The drive train affects how fast, powerful, and maneuverable the robot is. It plays a big role in:
How easily the robot can turn or strafe
How well it handles obstacles or ramps
How much control you have during precise movements
Battery efficiency and match performance
Q: What are some things to consider when choosing a drive train?
Mobility: Can it move in all directions or just forward/back?
Turning radius: Does it need to rotate in place?
Field challenges: Are there obstacles or terrain features?
Complexity: Is it easy to build and program?
Power needs: Will it strain the battery or motors?

## Slide 3: Why Does the Choice of Drive Train Matter?
Impact Areas:
  Speed: How fast the robot can move across the field
  Traction: Ability to grip the surface (important for ramps, pushing)
  Agility: How easily the robot can turn, strafe, or reposition
  Control: Precision in movement (critical for autonomous modes)
  Energy Efficiency: How much battery power it uses during a match
In Competition: A poorly chosen drive train can limit what your robot can do, no matter how good the other systems are!

## Slide 4: Choosing a Drive Train
Mobility Type:
Simple forward/backward? Omnidirectional (strafe, rotate in place)?
Field Obstacles:
Are there barriers, ramps, rough terrain?
Build & Programming Complexity:
Are you ready to handle more advanced construction and programming?
Weight and Power:
Heavier robots need more torque and stronger drive trains

## Slide 5: How Does Differential Drive Move?
Both wheels spin backward at the same speed.
Both wheels spin forward at the same speed.

## Slide 6: Differential Drive
A drive system where two wheels are independently powered by separate motors. The robot turns by spinning the wheels at different speeds.
Typical Layout:
  Two powered wheels (left and right)
  One or two passive casters (small free-rolling wheels) for balance
Simple but Powerful:
  Easy to build
  Easy to program
  Very reliable

## Slide 7: How Does Differential Drive Move?
Right wheel forward, left wheel backward = rotate counterclockwise
Right wheel spins faster or moves while left wheel slows/stops.

## Slide 8: Pros and Cons of Differential Drive
Pros:
Very simple to build and program
Great for driving in straight lines
Strong pushing power (good for defense tasks)
Highly reliable — fewer parts to fail
Cons:
Cannot strafe (no side-to-side movement)
Turning radius can be wide unless wheels rotate in opposite directions
Drag from passive casters can cause slight inaccuracies in autonomous movement

## Slide 9: Mecanum Drive Train
A Mecanum drive uses special wheels with angled rollers, allowing the robot to move in any direction — forward, backward, sideways (strafe), and diagonally — without changing its orientation.
Key Feature: The angled rollers on the wheels (usually 45°) create forces that combine to move the robot in complex ways.
Typical Layout: 4 Mecanum wheels, one on each corner of the robot.

## Slide 10: Mecanum Rollers

## Slide 11: How Mecanum Wheels Work
Each Wheel Pushes at an Angle:
Front-left and back-right wheels are mirrored.
Front-right and back-left wheels are mirrored.
Movement Control:
Combining wheel speeds and directions controls overall motion.
The robot's movement is the vector sum of forces from all four wheels.

## Slide 12: Motion Types with Mecanum Drive
Roboteq.com

## Slide 13: Motion Types with Mecanum Drive
Roboteq.com

## Slide 14: Motion Types with Mecanum Drive
Motion | Wheel Behavior
Forward | All wheels spin forward equally
Backward | All wheels spin backward equally
Strafe Right | Left wheels spin forward, right wheels spin backward
Strafe Left | Left wheels spin backward, right wheels spin forward
Rotate Clockwise | Front-left and back-left wheels spin backward, front-right and back-right spin forward
Diagonal Movement | Different combinations of wheels spinning faster/slower

## Slide 15: Pros and Cons of Mecanum Drive
Advantages:
  Full 360° movement — extremely maneuverable.
  Can move sideways without turning.
  Powerful for complex strategies (positioning, dodging, collecting).
Challenges:
  Requires precise motor control and tuning.
  Slight loss of force efficiency compared to traction wheels.
  Programming is more complex (requires vector math).
  Wheels are more expensive and delicate.

## Slide 16: X-Drive
An X-Drive uses omni wheels mounted at 45° angles to allow full omnidirectional movement.
Key Feature: Wheels directly face the robot’s movement directions — no angled rollers like Mecanum; the wheels themselves slide easily.
Typical Layout: 4 omni wheels placed in an "X" formation when viewed from above.

## Slide 17: X-Drive movement

## Slide 18: Pros and Cons of X-Drive
Pros:
  True omnidirectional motion
  Lighter and simpler mechanical build compared to Mecanum
  Easier math for programming (FTCLib or basic trig)
Cons:
  Lower pushing force (torque spread across angles)
  Frame must be rigid — any flex affects movement accuracy
  Not ideal for heavy robots

## Slide 19: Swerve Drive Trains
Swerve drive uses independent drive and steering for each wheel
Allows full omnidirectional movement and precise control
Each wheel module:
  Rotates (steers) 360°
  Drives forward/backward independently
Pros:
  Ultimate maneuverability
  Smooth diagonal motion and rotation in place
Cons:
  Mechanically and programmatically complex
  Heavy and expensive

## Slide 20: Swerve Drive Movement
Team 6624’s SW Guide

## Slide 21: Mars Rover Drive Systems
Rover | Wheels | Drive | Steering
Sojourner | 6 | Differential | No steering motors
Spirit | 6 | Independent | Front and rear steering
Opportunity | 6 | Independent | Front and rear steering
Curiosity | 6 | Independent | Front and rear steering
Perseverance | 6 | Independent | Front and rear steering (improved)
Zhurong | 6 | Independent | Front and rear steering
Notes: Drive System Details:
Independent Drive Motors: Each wheel has its own motor, allowing the rover to drive even if one wheel fails.
Steering Motors:
  Spirit, Opportunity, Curiosity, Perseverance: Front and rear wheels have independent steering motors.
  Perseverance: Has even more advanced wheel steering to reduce wheel wear and enable "crab walking" (moving diagonally).
Suspension System: All major Mars rovers use rocker-bogie suspension for stability on extremely rough terrain — it allows rovers to climb over rocks almost as tall as their wheels without tipping over.
Turning Type:
  Skid Steering (Sojourner) — turns by spinning wheels at different speeds (like a tank).
  Combined Steering (others) — steered wheels + independent drive for sharper, smoother turns.

## Slide 22: Curiosity Rover

## Slide 23: Rocker-Bogie Suspension
Rocker-bogie is a special suspension system that lets a rover keep all six wheels on the ground — even when climbing over big rocks or driving on uneven surfaces.
How It Works:
Rocker: Each side of the rover has a “rocker” arm that can pivot up and down independently.
Bogie: Each rocker connects to a "bogie" — a smaller pivoted beam that holds two wheels.
Balance: When one wheel climbs over an obstacle, the rocker and bogie flex to keep the rover stable and spread out the weight.

## Slide 24: Motors in Robotics
Powering Your Rover

## Slide 25: Why Motors Matter
Motors are the muscles of a robot
Convert electrical energy → mechanical motion
Essential for drive trains, arms, lifts, and more

## Slide 26: Types of Motors in Robotics
DC Motors: Continuous rotation, ideal for driving and lifting
Servo Motors: Limited range of motion, good for precise control
Stepper Motors: Precise, step-by-step rotation

## Slide 27: DC Motors
Most common motor type in robotics
Spin continuously in either direction
Speed and torque depend on voltage and gear ratio
Often paired with encoders for feedback

## Slide 28: GoBilda 5-Series Motors
Planetary gear motors with high reliability
5mm D-shaft, compact and modular
Compatible with FTC-standard building systems
We’ll be using the 312 RPM, 19.2:1 ratio motors in our drive trains

## Slide 29: Gear Ratios
Tells how many times the motor spins for one full turn of the output shaft
High gear ratio = more torque, less speed
Low gear ratio = more speed, less torque
Choose based on function:
  Drive train = moderate speed/torque
  Arm/lift = high torque
Our motor’s ratio is 19.2:1 - the motor spins 19.2 times for the output shaft to spin once

## Slide 30: Motor Direction and Power Basics
Motor power is set from -1 to 1:
  1 = full speed forward
  -1 = full speed in reverse
  0 = stop
Used to control speed and direction of movement
Default stop behavior at 0 power:
  Motors brake (resist movement)
  Can be changed to float if free movement is needed

## Slide 31: Programming a Motor
This sets the motor named "armMotor" to spin forward at 75% power
You can set power anywhere between -1 and 1
Use the setDirection method to REVERSE if needed.
Always match hardware names in code to those configured in the Control Hub
Notes: DcMotorEx leftMotor = hardwareMap.get(DcMotorEx.class, "armMotor");
leftMotor.setDirection(DcMotorSimple.Direction.FORWARD);
leftMotor.setPower(0.75);

## Slide 32: Motor Encoders
Motor Encoder is a sensor inside the motor that tracks how much it has rotated.
Reports motion in "ticks" or "counts"
Integrated encoders allow for:
  Precise speed control & position tracking
  Closed-loop feedback with PID
Software libraries provide motor control features
The 312 RPM motor has 537.6 ticks per shaft revolution
Notes: 🌀 What is an Encoder?
A sensor inside the motor that tracks how much it has rotated
Reports motion in "ticks" or "counts”
🔧 GoBilda 312 RPM Motor Specs:
Integrated encoder resolution: 28 counts per motor revolution
With a 19.2:1 gear ratio, this becomes:
  28 × 19.2 = 537.6 ticks per output shaft revolution
📏 What does that mean?
If your wheel is directly attached to the output shaft:
  1 full wheel rotation = ~538 encoder ticks
Want to drive the robot forward 1 wheel rotation?
  Set a target position of 538 ticks
🧠 Why it’s useful:
Measure how far the robot moves
Stop at precise locations (like lines or junctions)
Run motors to specific positions or hold them still
💡 In Code (FTCLib style):
motor.setTargetPosition(538); // one rotation
motor.setMode(RunMode.PositionControl);
motor.set(0.5); // move at 50% power

## Slide 33: Week #1 Goal
Build & code a Differential drive rover
Build & code a Mecanum drive rover
Compare performance