## Slide 1: Servos vs. Motors Quiz
Mission to Mars

## Slide 2
Which of the following is TRUE about DC motors? a) They move to a specific position and stop automatically b) They continuously spin when power is applied c) They require a control signal to set their angle d) They are only used in robotic arms

## Slide 3
What is a key feature of a servo motor that a regular DC motor lacks? a) Higher voltage range b) Gearbox for high speed c) Built-in position control d) Ability to run indefinitely

## Slide 4
When would you typically choose a servo motor over a DC motor? a) For driving wheels on a robot b) For turning a camera to a specific angle c) For generating electricity d) For powering a conveyor belt

## Slide 5
Which component is typically used with DC motors to monitor rotation? a) Resistor b) Encoder c) Potentiometer d) Switch

## Slide 6
What happens when power is cut off to a typical DC motor? a) It holds its position b) It moves to a zero-degree angle c) It continues spinning d) It stops spinning immediately

## Slide 7
Describe one scenario where using a DC motor would be better than using a servo.

## Slide 8
What is the role of an encoder when using DC motors in robotic applications?

## Slide 9
What kind of motor would you choose for a robot arm joint, and why?

## Slide 10
Name one advantage and one disadvantage of servo motors.

## Slide 11
Which of the following is TRUE about DC motors? b) They continuously spin when power is applied Explanation: DC motors spin as long as they're powered—they don’t stop at a specific angle unless additional control (like encoders) is used.
What is a key feature of a servo motor that a regular DC motor lacks? c) Built-in position control Explanation: Servos include internal circuitry and sensors to control position.
When would you typically choose a servo motor over a DC motor? b) For turning a camera to a specific angle Explanation: Servos are ideal for precise angular movement, such as pan-tilt mechanisms.
Which component is typically used with DC motors to monitor rotation? b) Encoder Explanation: Encoders help track position/speed for closed-loop control.
What happens when power is cut off to a typical DC motor? d) It stops spinning immediately Explanation: DC motors lose all torque when power is removed.

## Slide 12
Describe one scenario where using a DC motor would be better than using a servo. Example Answer: Driving a robot’s wheels, where continuous rotation and higher torque are needed. Explanation: Servos have limited range and are not ideal for drivetrain movement.
How does a servo motor "know" what position it is in? Answer: It uses a built-in potentiometer or sensor to detect shaft angle and adjusts itself to match the commanded position.
What is the role of an encoder when using DC motors in robotic applications? Answer: Encoders provide feedback on shaft rotation or speed, enabling the use of PID control for accurate movement.
What kind of motor would you choose for a robot arm joint, and why? Answer: A servo motor, because it provides precise control of angle and can hold a set position. Optional: A high-torque servo is preferred for heavier arms.
Name one advantage and one disadvantage of servo motors. Advantage: Built-in position control. Disadvantage: Limited rotation range and lower continuous torque compared to DC motors.